## Slide 1: Changing The Yamaha IT175J Lower Steering Stem Bearing.

## Slide 2: Health and Safety
The procedures depicted here have been performed by a professional Engineer.
Please do not attempt any of these operations unless you have been deemed to be a competent person.
Wear the correct PPE, adhere to appropriate Health and Safety guidelines and dispose of any wastes created in accordance with local regulations.

## Slide 3: Step one…. Get someone else to do it !

## Slide 4: Maybe not !

## Slide 5: I’ll do it myself then.

## Slide 6: That’s not one of my better ideas !

## Slide 7: Steering stem support spigot, spacer and pressing sleeve made up from scrap material.

## Slide 8: It just fell apart ! That’s my old IT490 sprockets in the background !

## Slide 9: Spacer made from old water pipe.

## Slide 10: Spacer needs to be central during stem and bearing removal.

## Slide 11: Bottom yolk assembly carefully lined up in the trusty ‘Epco’ press.

## Slide 12: Worn bearing now free from the steering stem. Removing the bearing and stem required about 2000 psi hydraulic pressure.

## Slide 13: Showing steering stem support spigot position.

## Slide 14: Steering stem lubricated and nicely lined up.

## Slide 15: Steering stem pressed into position. This operation required about 1000 psi.

## Slide 16: New, correct style bearing waiting to be pressed into place. Oil or grease the stem before pressing on the bearing.

## Slide 17: Once again, make sure everything is square and true before applying pressure.

## Slide 18: Whoa there ! Bearing pressed into place. Fitting the bearing only required only about 250 psi.

## Slide 19: Ready to be fitted to the bike. Don’t forget to grease the bearings liberally before installation.

## Slide 20: CREDITS !
To my Daughter for getting this PowerPoint presentation to work ( Yet again ! ).
Members of the Aussie IT forum.http://www.yamahait.com.au/ for their support.
My work place for putting up with me !